## Slide 1: Attitude Representations
Quick & Dirty for use in software

## Slide 2: Representing Attitude
There are several ways to represent the rotation between two reference frames
    Direction Cosines
    Euler Angles
    Quaternions (aka Euler Parameters)
    and more
They all have their strengths and weaknesses

## Slide 3: Strengths and Weaknesses of Attitude Representations
Representation | Strengths | Weaknesses | Best Used For
Direction Cosines | Work well with vectors Easy to catenate rotations Moderately intuitive (dot products) No singularities | 9 params for 3 DOF | Transforming Vectors
Quaternions | Efficient (4 params for 3 DOF) No singularities | Not intuitive | Propagating Equations of Motion
Euler Angles | Intuitive 3 params for 3DOF | Singularities 12 Variants | Input, Output Gimballed Joints

## Slide 4: Euler Angles
Chronologically first in aerospace applications.
Generally works well for airplanes
  Angles tend to be small deviations from the velocity frame
Good especially for small values
  For small values, rotations approximately commute.
Satellite GNC used Euler angles for primary design into 1970’s.
  Not great for satellites because satellites have arbitrarily large attitude deviations.
  Control on euler angles highly non-linear
  Euler angles and all three-parameter attitude descriptions have a singularity

## Slide 5: Singularities
For high pitch, a small rotation
creates a large Yaw change

## Slide 6: Non-commutative

## Slide 7: Euler’s Rotation Theorem (1776)

## Slide 8: Euler’s Rotation Theorem
n
θ
Theorema. Quomodocunque sphaera circa centrum suum conuertatur, semper assignari potest diameter, cuius directio in situ translato conueniat cum situ initiali.

## Slide 9: Euler’s Rotation Theorem
When a sphere is moved around its centre it is always possible to find a diameter whose direction in the displaced position is the same as in the initial position.

## Slide 10: Euler Theorem in German
Egal wie sich die Kugel um ihren Mittelpunkt dreht, ihr kann immer ein Durchmesser zugeordnet werden, dessen Richtung in der Translationslage mit der Ausgangslage übereinstimmt.
Butterfly
Papillon
Farfalla
Fluture
Schmetterling

## Slide 11: Direction Cosine Matrix (DCM)

## Slide 12: Quaternions

## Slide 13: What a quaternion looks like

## Slide 14: Quaternion Notation Issues
Excerpt from https://www.astro.rug.nl/software/kapteyn-beta/_downloads/attitude.pdf
To eliminate ambiguity we represent a quaternion:
= =
Scalar part
My notation (and JPL, 42’s) mimics DCM notation
Hamiltonian Notation
Image Processing Might Used Conventions that differ from GNC!
Scalar part

## Slide 15
https://www.researchgate.net/publication/323426570_Why_and_How_to_Avoid_the_Flipped_Quaternion_Multiplication_-_Shorter_and_Less_Formal_Version

## Slide 16: DCM’s & Quaternions

## Slide 17: Matlab Interlude

## Slide 18: Properties of Rotations

## Slide 19: Notation for Quaternions, DCMs
The rotation from frame A to frame B may be described by the direction cosine matrix
Given the components of a vector in A, its components in B may be found by the multiplication
In C, we write the DCM as CBA to preserve order of superscripts, eg
Quaternions are another way to describe rotations. We use a parallel notation:
These and similar conventions promote concise, unambiguous code
MxV(CBA,va,vb)
QxV(qba,va,vb)

## Slide 20: References
http://www.opengl-tutorial.org/intermediate-tutorials/tutorial-17-quaternions/
https://en.wikipedia.org/wiki/Euler%27s_rotation_theorem
https://www.astro.rug.nl/software/kapteyn-beta/_downloads/attitude.pdf
https://fzheng.me/2017/11/12/quaternion_conventions_en/
http://www.iri.upc.edu/people/jsola/JoanSola/objectes/notes/kinematics.pdf
https://www.researchgate.net/publication/323426570_Why_and_How_to_Avoid_the_Flipped_Quaternion_Multiplication_-_Shorter_and_Less_Formal_Version